## Slide 1: Swift Burst Alert Telescope
Caltech X-ray Club, 2020/10/13
Amy Lien
Goddard Space Flight Center

## Slide 2: Outline
Exploring the Universe with BAT
BAT instrument
  BAT detectors
  Coded aperture method
BAT data product
  BAT GRB catalog
  BAT transient monitor
  BAT survey catalog
Finding weak sources in BAT

## Slide 3
Burst Alert Telescope (BAT)
X-Ray Telescope (XRT)
UV/Optical Telescope (UVOT)
Gehrels et al. (2004)
Neil Gehrels Swift Observatory
BAT science Coded mask BAT products Weak sources Summary

## Slide 4
Burst Alert Telescope (BAT)
X-Ray Telescope (XRT)
UV/Optical Telescope (UVOT)
Gehrels et al. (2004)
Neil Gehrels Swift Observatory
Launched in Nov. 20, 2004
Dedicated for GRB study
Extend beyond GRB science and has become an observatory that serves a much wider community
BAT science Coded mask BAT products Weak sources Summary

## Slide 5
Burst Alert Telescope (BAT)
Gehrels et al. (2004)
Neil Gehrels Swift Observatory
BAT science Coded mask BAT products Weak sources Summary

## Slide 6: Burst Alert Telescope (BAT)
Responsible for finding GRBs
15-350 keV
Large field of view (~ 1/6 of the sky)  Increase the number of GRB detections
  ~1.4 sr (half coded)
  ~ 2 sr (fully coded)
Decent localization in hard X rays (~ 3 arcmin)  Enable prompt follow-up of narrow field instruments
BAT science Coded mask BAT products Weak sources Summary

## Slide 7: Swift GRBs to date: 15.9 Years after Launch
1326 GRBs (～ two per week)
459 GRBs with distance measurements
Swift/BAT GRB catalog:
https://swift.gsfc.nasa.gov/results/batgrbcat/
BAT science Coded mask BAT products Weak sources Summary

## Slide 8: 15.9 Years of Swift
Chart: 
| GRBs | Other | SAA | Cal
Column1 | 15 | 64 | 18 | 3
Figure credit: PSU webpage
Ref: Swift 2019 Senior Review Proposal
Other
SAA
Chart: 
| GRBs | Other | SAA | Cal
Column1 | 46 | 19 | 18 | 17
GRBs
SAA
Cal
Other
Fractional Observing Time
2005
2018
46%
19%
18%
17%
62%
17%
3%
18%
GRBs
BAT science Coded mask BAT products Weak sources Summary

## Slide 9: 15.9 Years of Swift
Chart: 
| GRBs | Other | SAA | Cal
Column1 | 15 | 64 | 18 | 3
Figure credit: PSU webpage
Ref: Swift 2019 Senior Review Proposal
Other
GRBs
SAA
Chart: 
| GRBs | Other | SAA | Cal
Column1 | 46 | 19 | 18 | 17
GRBs
SAA
Cal
Other
Fractional Observing Time
2005
2018
46%
19%
18%
17%
62%
17%
3%
18%
BAT science Coded mask BAT products Weak sources Summary

## Slide 10: Beyond GRBs Exploring the Universe with BAT
Credit: Topics of Swift GI proposals someone’s talk at Penn State
BAT science Coded mask BAT products Weak sources Summary

## Slide 11: Beyond GRBs Exploring the Universe with BAT
BAT triggers on sources beyond GRBs. E.g.,
  Soft Gamma-ray Repeaters (SGRs)
BAT light curve on the forests of bursts
from recent activities of SGR 1935+2154 related to fast radio bursts
Credit: David Palmer
BAT science Coded mask BAT products Weak sources Summary

## Slide 12: Beyond GRBs Exploring the Universe with BAT
BAT triggers on sources beyond GRBs. E.g.,
  Soft Gamma-ray Repeaters (SGRs)
A new SGR just triggered by BAT last Saturday!
BAT science Coded mask BAT products Weak sources Summary

## Slide 13: Beyond GRBs Exploring the Universe with BAT
BAT triggers on sources beyond GRBs. E.g.,
  Soft Gamma-ray Repeaters (SGRs)
  Tidal disruption event
Burrows et al. (2011)
Credit: nasa.gov
BAT science Coded mask BAT products Weak sources Summary

## Slide 14: Beyond GRBs Exploring the Universe with BAT
BAT triggers on sources beyond GRBs. E.g.,
  Soft Gamma-ray Repeaters (SGRs)
  Tidal disruption event
Long-term monitoring of hard X-ray sources
  Monitoring > 2000 known sources
  ~ 16 years and counting…
BAT transient monitor daily light curve
Krimm et al. (2013)
BAT science Coded mask BAT products Weak sources Summary

## Slide 15: Beyond GRBs Exploring the Universe with BAT
BAT triggers on sources beyond GRBs. E.g.,
  Soft Gamma-ray Repeaters (SGRs)
  Tidal disruption event
Long-term monitoring of hard X-ray sources
  Monitoring > 2000 known sources
  ~ 16 years and counting…
Deep hard X-ray survey on mosaic images throughout the entire mission time.
BAT science Coded mask BAT products Weak sources Summary

## Slide 16: Beyond GRBs Exploring the Universe with BAT
Oh et al. (2018)
BAT science Coded mask BAT products Weak sources Summary

## Slide 17: Beyond GRBs Exploring the Universe with BAT
BAT triggers on sources beyond GRBs. E.g.,
  Soft Gamma-ray Repeaters (SGRs)
  Tidal disruption event
Long-term monitoring of hard X-ray sources
  Monitoring > 2000 known sources
  ~ 16 years and counting…
Deep hard X-ray survey on mosaic images throughout the entire mission time.
BAT science Coded mask BAT products Weak sources Summary

## Slide 18
BAT triggers on sources beyond GRBs. E.g.,
  Soft Gamma-ray Repeaters (SGRs)
  Tidal disruption event
Long-term monitoring of hard X-ray sources
  Monitoring > 2000 known sources
  ~ 16 years and counting…
Deep hard X-ray survey on mosaic images throughout the entire mission time.
Numerous counterpart searches
BAT science Coded mask BAT products Weak sources Summary
Beyond GRBs Exploring the Universe with BAT

## Slide 19: Beyond GRBs Exploring the Universe with BAT
GW counterpart searches
FRB counterpart searches
Cunningham et al. 2019
Lien et al. 2019
BAT science Coded mask BAT products Weak sources Summary

## Slide 20: Beyond GRBs Exploring the Universe with BAT
Oh et al. (2018)
AT2018cow: A white dwarf tidal disruption event?
(Kuin et al. 2018)
Fig credit: Fermi/LAT
The largest glitch observed in the Crab pulsar
(Shaw et al. MNRAS, 2018)
Multi-wavelength characterization of the blazar S5 0716+714
during an unprecedented outburst phase
(MAGIC Collaboration, A&A, 2018)
Multiwavelength follow-up of a rare IceCube neutrino multiplet
(IceCube Collaboration, A&A, 2017)
BAT science Coded mask BAT products Weak sources Summary

## Slide 21: Beyond GRBs Exploring the Universe with BAT
BAT triggers on sources beyond GRBs. E.g.,
  Soft Gamma-ray Repeaters (SGRs)
  Tidal disruption event
Long-term monitoring of hard X-ray sources
  Monitoring > 2000 known sources
  ~ 16 years and counting…
Deep hard X-ray survey on mosaic images throughout the entire mission time.
Numerous counterpart searches
BAT science Coded mask BAT products Weak sources Summary

## Slide 22: Beyond GRBs Exploring the Universe with BAT
BAT triggers on sources beyond GRBs:
  Soft Gamma-ray Repeaters (SGRs)
  Tidal disruption event
Long-term monitoring of hard X-ray sources
  Monitoring > 2000 known sources
  ~ 16 years and counting…
Deep hard X-ray survey on mosaic images throughout the entire mission time.
Numerous counterpart searches
Achievable thanks to
Large field of view
Decent localization
in hard X ray.
BAT science Coded mask BAT products Weak sources Summary

## Slide 23: Beyond GRBs Exploring the Universe with BAT
BAT triggers on sources beyond GRBs:
  Soft Gamma-ray Repeaters (SGRs)
  Tidal disruption event
Long-term monitoring of hard X-ray sources
  Monitoring > 2000 known sources
  ~ 16 years and counting…
Deep hard X-ray survey on mosaic images throughout the entire mission time.
Numerous counterpart searches
Achievable thanks to
Large field of view
Decent localization
in hard X ray.
Coded mask technique
BAT science Coded mask BAT products Weak sources Summary

## Slide 24: Coded-mask technique
Fig credit: Hullinger et al. 2006
BAT science Coded mask BAT products Weak sources Summary

## Slide 25: Coded-mask technique
Credit: NASA/Swift webpage
Fig credit: Hullinger et al. (2006)
BAT science Coded mask BAT products Weak sources Summary
Notes: 1 min
Tot: 7:30

## Slide 26: Coded-mask technique
Credit: NASA/Swift webpage
Coded Aperture Mask
BAT science Coded mask BAT products Weak sources Summary

## Slide 27: Coded-mask technique
Credit: NASA/Swift webpage
BAT detector array
BAT science Coded mask BAT products Weak sources Summary

## Slide 28: Coded-mask technique
Credit: NASA/Swift webpage
BAT detectors:
32,768 CZT (CdZnTe) detectors
Energy range:
15-350 keV for detection
(15-200 keV for imaging)
A Detector Module (128*2 detectors)
BAT science Coded mask BAT products Weak sources Summary

## Slide 29: Coded-mask technique
Credit: NASA/Swift webpage
BAT science Coded mask BAT products Weak sources Summary

## Slide 30: Coded-mask technique
Markwardt et al. (2007)
Barthelmy et al. (2005)
BAT science Coded mask BAT products Weak sources Summary

## Slide 31: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
BAT science Coded mask BAT products Weak sources Summary

## Slide 32: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
BAT science Coded mask BAT products Weak sources Summary

## Slide 33: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
1
1
1
0.8
0.6
0.9
0.5
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Assigning weights
(wi)
BAT science Coded mask BAT products Weak sources Summary
Notes: maskwtcorrs.c
* maskwtnorm - compute mask weight normalization
*
* The mask weighting technique (i.e. mask-detector cross correlation)
* produces an image with units of "counts" but with a more or less
* arbitrary intensity scale. This routine computes the normalization
* based on the mask-detector geometry, and assuming the distribution
* of illumination fractions is known.
*
* double srcpos[3] - source position in BAT_X/Y/Z (cm)
* struct batmaskplane_struct *mask - mask orientation
* struct batdetplane_struct *detplane - detector plane orientation
*
* RETURNS: mask weight technique normalization.
* Users are meant to take (maskwtval)/(maskwtnorm) to arrive at
* the true sky counts, where maskwtval is the weighted sum
* measured from the detector data.

## Slide 34: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
1
1
1
0.8
0.6
0.9
0.5
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Rebalancing
Sum(wi) = 0
 So background average to zero
BAT science Coded mask BAT products Weak sources Summary
Notes: maskwtcorrs.c
* maskwtnorm - compute mask weight normalization
*
* The mask weighting technique (i.e. mask-detector cross correlation)
* produces an image with units of "counts" but with a more or less
* arbitrary intensity scale. This routine computes the normalization
* based on the mask-detector geometry, and assuming the distribution
* of illumination fractions is known.
*
* double srcpos[3] - source position in BAT_X/Y/Z (cm)
* struct batmaskplane_struct *mask - mask orientation
* struct batdetplane_struct *detplane - detector plane orientation
*
* RETURNS: mask weight technique normalization.
* Users are meant to take (maskwtval)/(maskwtnorm) to arrive at
* the true sky counts, where maskwtval is the weighted sum
* measured from the detector data.

## Slide 35: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
1
1
1
0.8
0.6
0.9
0.5
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Uniform bkg:
1 ct/pix
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Weight (wi)
Imagine there is a uniform background
of 1 photon per detector
BAT science Coded mask BAT products Weak sources Summary
Notes: maskwtcorrs.c
* maskwtnorm - compute mask weight normalization
*
* The mask weighting technique (i.e. mask-detector cross correlation)
* produces an image with units of "counts" but with a more or less
* arbitrary intensity scale. This routine computes the normalization
* based on the mask-detector geometry, and assuming the distribution
* of illumination fractions is known.
*
* double srcpos[3] - source position in BAT_X/Y/Z (cm)
* struct batmaskplane_struct *mask - mask orientation
* struct batdetplane_struct *detplane - detector plane orientation
*
* RETURNS: mask weight technique normalization.
* Users are meant to take (maskwtval)/(maskwtnorm) to arrive at
* the true sky counts, where maskwtval is the weighted sum
* measured from the detector data.

## Slide 36: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
1
1
1
0.8
0.6
0.9
0.5
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Uniform bkg:
1 ct/pix
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Weight (wi)
Imagine there is a uniform background
of 1 photon per detector
Mask-weighted count for this source location:
Sum(bkg*wi) = 1*0.8 + 1*1 + 1*1 + 1*1 + 1*0.6 + 1*0.5 + 1*0.9 = 5.8
BAT science Coded mask BAT products Weak sources Summary
Notes: maskwtcorrs.c
* maskwtnorm - compute mask weight normalization
*
* The mask weighting technique (i.e. mask-detector cross correlation)
* produces an image with units of "counts" but with a more or less
* arbitrary intensity scale. This routine computes the normalization
* based on the mask-detector geometry, and assuming the distribution
* of illumination fractions is known.
*
* double srcpos[3] - source position in BAT_X/Y/Z (cm)
* struct batmaskplane_struct *mask - mask orientation
* struct batdetplane_struct *detplane - detector plane orientation
*
* RETURNS: mask weight technique normalization.
* Users are meant to take (maskwtval)/(maskwtnorm) to arrive at
* the true sky counts, where maskwtval is the weighted sum
* measured from the detector data.

## Slide 37: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
1
1
1
0.8
0.6
0.9
0.5
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
Uniform bkg:
1 ct/pix
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
Weight (wi)
Imagine there is a uniform background
of 1 photon per detector
Mask-weighted count for this source location:
Sum(bkg*wi) = 1*0.8 + 1*1 + 1*1 + 1*1 + 1*0.6 + 1*0.5 + 1*0.9 = 5.8
But we know this is just background,
So we would like the resulting mask-weighting count to be zero
Rebalacing (for example, wi-0.1)
Sum(bkg*(wi-0.1)) = 1*0.7 + 1*0.9 + 1*0.9 + 1*0.9 + 1*0.5 + 1*0.4 + 1*0.8
– 0.1*(rest of the detector weights)
= 0
BAT science Coded mask BAT products Weak sources Summary
Notes: maskwtcorrs.c
* maskwtnorm - compute mask weight normalization
*
* The mask weighting technique (i.e. mask-detector cross correlation)
* produces an image with units of "counts" but with a more or less
* arbitrary intensity scale. This routine computes the normalization
* based on the mask-detector geometry, and assuming the distribution
* of illumination fractions is known.
*
* double srcpos[3] - source position in BAT_X/Y/Z (cm)
* struct batmaskplane_struct *mask - mask orientation
* struct batdetplane_struct *detplane - detector plane orientation
*
* RETURNS: mask weight technique normalization.
* Users are meant to take (maskwtval)/(maskwtnorm) to arrive at
* the true sky counts, where maskwtval is the weighted sum
* measured from the detector data.

## Slide 38: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
1
1
1
0.8
0.6
0.9
0.5
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
-0.1
Rebalancing
Sum(wi) = 0
 So background average to zero
BAT science Coded mask BAT products Weak sources Summary
Notes: maskwtcorrs.c
* maskwtnorm - compute mask weight normalization
*
* The mask weighting technique (i.e. mask-detector cross correlation)
* produces an image with units of "counts" but with a more or less
* arbitrary intensity scale. This routine computes the normalization
* based on the mask-detector geometry, and assuming the distribution
* of illumination fractions is known.
*
* double srcpos[3] - source position in BAT_X/Y/Z (cm)
* struct batmaskplane_struct *mask - mask orientation
* struct batdetplane_struct *detplane - detector plane orientation
*
* RETURNS: mask weight technique normalization.
* Users are meant to take (maskwtval)/(maskwtnorm) to arrive at
* the true sky counts, where maskwtval is the weighted sum
* measured from the detector data.

## Slide 39: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
0.9
0.9
0.9
0.7
0.6
0.8
0.4
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
Rebalancing
Sum(wi) = 0
 So background average to zero
BAT science Coded mask BAT products Weak sources Summary
Notes: maskwtcorrs.c
* maskwtnorm - compute mask weight normalization
*
* The mask weighting technique (i.e. mask-detector cross correlation)
* produces an image with units of "counts" but with a more or less
* arbitrary intensity scale. This routine computes the normalization
* based on the mask-detector geometry, and assuming the distribution
* of illumination fractions is known.
*
* double srcpos[3] - source position in BAT_X/Y/Z (cm)
* struct batmaskplane_struct *mask - mask orientation
* struct batdetplane_struct *detplane - detector plane orientation
*
* RETURNS: mask weight technique normalization.
* Users are meant to take (maskwtval)/(maskwtnorm) to arrive at
* the true sky counts, where maskwtval is the weighted sum
* measured from the detector data.

## Slide 40: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
0.9
0.9
0.9
0.7
0.6
0.8
0.4
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
-0.1
Mask-weighted count can be negative, but will average to zero during background period.
BAT science Coded mask BAT products Weak sources Summary
Notes: maskwtcorrs.c
* maskwtnorm - compute mask weight normalization
*
* The mask weighting technique (i.e. mask-detector cross correlation)
* produces an image with units of "counts" but with a more or less
* arbitrary intensity scale. This routine computes the normalization
* based on the mask-detector geometry, and assuming the distribution
* of illumination fractions is known.
*
* double srcpos[3] - source position in BAT_X/Y/Z (cm)
* struct batmaskplane_struct *mask - mask orientation
* struct batdetplane_struct *detplane - detector plane orientation
*
* RETURNS: mask weight technique normalization.
* Users are meant to take (maskwtval)/(maskwtnorm) to arrive at
* the true sky counts, where maskwtval is the weighted sum
* measured from the detector data.

## Slide 41: Mask-weighted light curve
BAT science Coded mask BAT products Weak sources Summary

## Slide 42: Mask-weighted light curve
BAT science Coded mask BAT products Weak sources Summary

## Slide 43
～ 120 degree
～ 90 degree
Detector Plane Image
Reconstructed Sky Image
GRB
Image reconstruction
BAT science Coded mask BAT products Weak sources Summary

## Slide 44: Partial coding fraction
Fraction of illuminated area
Source comes in from the zenith (0 deg boresight angle): pcode = 1
Source out of the field of view: pcode = 0
Larger pcode means more detectors are illuminated by the source, and thus BAT is more sensitive to the source.
BAT science Coded mask BAT products Weak sources Summary

## Slide 45: Partial coding fraction
pcode = 1
theta = 0 deg
BAT science Coded mask BAT products Weak sources Summary

## Slide 46: Partial coding fraction
pcode = 0.5
theta = 29 deg
29o
BAT science Coded mask BAT products Weak sources Summary

## Slide 47: Partial coding fraction
pcode = 0.04
theta = 50 deg
50o
BAT science Coded mask BAT products Weak sources Summary

## Slide 48: Partial coding fraction vs BAT effective area
Ref: https://swift.gsfc.nasa.gov/analysis/bat_digest.html
BAT science Coded mask BAT products Weak sources Summary

## Slide 49: Partial coding fraction vs BAT field of view
BAT science Coded mask BAT products Weak sources Summary

## Slide 50: Mask-weighted count
BAT science Coded mask BAT products Weak sources Summary

## Slide 51: Mask-weighted count
Definition:
Background subtracted counts
per fully illuminated detector
for an equivalent on-axis source
Ref: https://swift.gsfc.nasa.gov/analysis/threads/batfluxunitsthread.html
BAT science Coded mask BAT products Weak sources Summary

## Slide 52: Mask-weighted count
Definition:
Background subtracted counts
per fully illuminated detector
for an equivalent on-axis source
Ref: https://swift.gsfc.nasa.gov/analysis/threads/batfluxunitsthread.html
Illuminated detector ～ # of enabled detector x pcode
BAT science Coded mask BAT products Weak sources Summary

## Slide 53: Mask-weighted count
Definition:
Background subtracted counts
per fully illuminated detector
for an equivalent on-axis source
Ref: https://swift.gsfc.nasa.gov/analysis/threads/batfluxunitsthread.html
cos(θ) effect
BAT science Coded mask BAT products Weak sources Summary

## Slide 54: Summery of coded mask instrument
Pros:
  Large field of view
  Decent localization for hard X ray
  Decent background estimation
Cons:
  Reduced sensitivity for the same number of detectors
  (mask covers > half of the detectors)
  Challenging to deal with diffuse sources
  All sources in the field of view will contribute to the noise
Sensitivity depends on the partial coding fraction
BAT science Coded mask BAT products Weak sources Summary

## Slide 55: Exploring the Universe with BAT
BAT science Coded mask BAT products Weak sources Summary

## Slide 56: BAT data type
DATA type | Description | Energy range | Can generate Image? | Time bin | Continuous?
Event data | Complete info of each photon | All | ✔ | Customizable (> 100 us) | ✗
Survey data | Pre-binned detector plane image | 80 channels (14-195 keV) | ✔ | ~ 300 s | ✔ (except during SAA and slew)
Scaled map data | Detector plane scaled map for image triggers | 15-50 keV | ✔ | ~ 8 s | ✔ (except during SAA and slew)
Rate data | Raw (not background subtracted) light curves | 4 channels (15-25, 25-50, 50-100,100-350 keV) | ✗ | 64 ms, 1 s, 1.6 s | ✔
For more info, see Markwardt et al. (2007)
BAT science Coded mask BAT products Weak sources Summary

## Slide 57: BAT public products
BAT GRB catalog (event data)
  https://swift.gsfc.nasa.gov/results/batgrbcat/
BAT transient monitor (scaled map data)
  https://swift.gsfc.nasa.gov/results/transients/
BAT survey catalog (survey data)
  https://swift.gsfc.nasa.gov/results/bs105mon/
BAT science Coded mask BAT products Weak sources Summary

## Slide 58: BAT transient monitor
Krimm et al. (2013)
Product made from scaled map data
https://swift.gsfc.nasa.gov/results/transients/
Energy range: 15-50 keV
Monitoring > 1000 sources
  daily light curves
  orbital light curves (time bins of ~ 64 second up to a couple thousand second).
Updated every few hours
If you’d like to add your favorite source to the monitoring list, send me an email!
BAT science Coded mask BAT products Weak sources Summary

## Slide 59: BAT survey catalogs
Product made from BAT survey data
  Source detections on mosaic images
Existing BAT survey catalog
  3-month (Markwardt et al. 2005)
  22-month (Tueller et al. 2008)
  70-month (Baumgartner et al. 2013)
  105-month (Oh et al. 2018)
  Upcoming: 157-month (Lien et al. 2021 in prep)
  Other BAT survey catalogs:
  (using different analysis process)
    The Palermo Swift-BAT Hard X-ray Catalogs
      39-month, 54-month, (Cusumano et al. 2010)
    60-month (Ajello et al., 2012)
    3-year (Burlon & Ajello et al. 2011)
BAT science Coded mask BAT products Weak sources Summary

## Slide 60: BAT survey exposure time
Oh et al. (2018)
BAT science Coded mask BAT products Weak sources Summary

## Slide 61: BAT sensitivity
Eq. 9, Baumgardner et al. (2013)
1 mCrab = 2.42 x 10-11 erg/s/cm2
2.42 x 10-11
2.42 x 10-10
2.42 x 10-12
9.86 x 10-12
9.86 x 10-11
BAT science Coded mask BAT products Weak sources Summary

## Slide 62: BAT sensitivity
Eq. 9, Baumgartner et al. (2013)
1 mCrab = 2.42 x 10-11 erg/s/cm2
2.42 x 10-11
2.42 x 10-10
2.42 x 10-12
9.86 x 10-12
9.86 x 10-11
BAT science Coded mask BAT products Weak sources Summary
GRB detections
Lien et al. (2016)

## Slide 63: BAT sensitivity
Eq. 9, Baumgardner et al. (2013)
1 mCrab = 2.42 x 10-11 erg/s/cm2
2.42 x 10-11
2.42 x 10-10
2.42 x 10-12
9.86 x 10-12
9.86 x 10-11
BAT science Coded mask BAT products Weak sources Summary

## Slide 64: BAT survey catalogs
Markwardt et al. (2005); Tueller et al. (2008); Tueller et al. (2010); Baumgartner et al. (2013); Oh et al. (2018)
1 mCrab = 2.42 x 10-11 erg/s/cm2
2.42 x 10-11
2.42 x 10-10
2.42 x 10-12
9.86 x 10-12
9.86 x 10-11
BAT science Coded mask BAT products Weak sources Summary

## Slide 65: BAT survey catalogs
Oh et al. (2018)
Product at: https://swift.gsfc.nasa.gov/results/bs105mon/
- From Dec. 2004 to Aug. 2013.
- Monthly light curves, spectra…etc.
105 month
BAT science Coded mask BAT products Weak sources Summary

## Slide 66: BAT survey catalogs
1 mCrab = 2.42 x 10-11 erg/s/cm2
2.42 x 10-11
2.42 x 10-10
2.42 x 10-12
9.86 x 10-12
9.86 x 10-11
Markwardt et al. (2005); Tueller et al. (2008); Tueller et al. (2010); Baumgartner et al. (2013); Oh et al. (2018)
Coming up:
157 month catalog (end at Dec. 2017)
https://swift.gsfc.nasa.gov/results/bs157mon/
Monthly update of survey products
BAT science Coded mask BAT products Weak sources Summary

## Slide 67: BAT survey catalogs
Markwardt et al. (2005); Tueller et al. (2008); Tueller et al. (2010); Baumgartner et al. (2013); Oh et al. (2018)
1 mCrab = 2.42 x 10-11 erg/s/cm2
2.42 x 10-11
2.42 x 10-10
2.42 x 10-12
9.86 x 10-12
9.86 x 10-11
BAT science Coded mask BAT products Weak sources Summary

## Slide 68: What if your favorite source is not in the public catalogs?
(Send me an email)
Do your own search
  All Swift data are available on HEASARC:
https://heasarc.gsfc.nasa.gov/cgi-bin/W3Browse/swift.pl
BAT science Coded mask BAT products Weak sources Summary

## Slide 69: Will your sources be detected in BAT?
BAT science Coded mask BAT products Weak sources Summary
Eq. 9, Baumgardner et al. (2013)
1 mCrab = 2.42 x 10-11 erg/s/cm2
2.42 x 10-11
2.42 x 10-10
2.42 x 10-12
9.86 x 10-12
9.86 x 10-11

## Slide 70: What is a real detection?
What counts as a detection in BAT?
  BAT onboard trigger algorithm: over 600 trigger criteria with different count rate threshold, ~ 7 sigma for image threshold.
  BAT survey catalog: 4.8 sigma.
    1.54 false detections
    in the mosaic sky map
    of 1.99 x 106 pixels
    (Tueller et al. 2010).
BAT science Coded mask BAT products Weak sources Summary
Tueller et al. (2010)

## Slide 71: What is a real detection?
BAT science Coded mask BAT products Weak sources Summary

## Slide 72: What is a real detection?
BAT science Coded mask BAT products Weak sources Summary
Sub-threshold events

## Slide 73: Looking for dim signals in BAT: Things to be aware of
Any sources in the FOV will affect the noise/flux estimation for your interested source.
BAT noise generally follows Gaussian statistics, however, we do see slight divergence from Gaussian, which might be especially important for sub-threshold signals.
More systematic noise at the edge of the field of view.
Be cautious of sources under ~ 7 sigma in an image.
There is additional systematic noise when integrating over ~ a few days (patter noise).
Detector noise that mimics a burst.
BAT science Coded mask BAT products Weak sources Summary

## Slide 74: Looking for dim signals in BAT: Things to be aware of
Any sources in the FOV will affect the noise/flux estimation for your interested source.
BAT noise generally follows Gaussian statistics, however, we do see slight divergence from Gaussian, which might be especially important for sub-threshold signals.
More systematic noise at the edge of the field of view.
Be cautious of sources under ~ 7 sigma in an image.
There is additional systematic noise when integrating over ~ a few days (patter noise).
Detector noise that mimics a burst.
BAT science Coded mask BAT products Weak sources Summary

## Slide 75: Looking for dim signals in BAT: Things to be aware of
Any sources in the FOV will affect the noise/flux estimation for your interested source.
BAT noise generally follows Gaussian statistics, however, we do see slight divergence from Gaussian, which might be especially important for sub-threshold signals.
More systematic noise at the edge of the field of view.
Be cautious of sources under ~ 7 sigma in an image..
There is additional systematic noise when integrating over ~ a few days (patter noise).
Detector noise that mimics a burst.
BAT science Coded mask BAT products Weak sources Summary

## Slide 76: Looking for dim signals in BAT: Things to be aware of
Any sources in the FOV will affect the noise/flux estimation for your interested source.
BAT noise generally follows Gaussian statistics, however, we do see slight divergence from Gaussian, which might be especially important for sub-threshold signals.
More systematic noise at the edge of the field of view.
Be cautious of sources under ~ 7 sigma in an image.
There is additional systematic noise when integrating over ~ a few days (patter noise).
Detector noise that mimics a burst.
BAT science Coded mask BAT products Weak sources Summary

## Slide 77: Looking for dim signals in BAT: Things to be aware of
Any sources in the FOV will affect the noise/flux estimation for your interested source.
BAT noise generally follows Gaussian statistics, however, we do see slight divergence from Gaussian, which might be especially important for sub-threshold signals.
More systematic noise at the edge of the field of view.
Be cautious of sources under ~ 7 sigma in an image.
There is additional systematic noise when integrating over ~ a few days (patter noise).
Detector noise that mimics a burst.
BAT science Coded mask BAT products Weak sources Summary

## Slide 78: Looking for dim signals in BAT: Things to be aware of
Any sources in the FOV will affect the noise/flux estimation for your interested source.
BAT noise generally follows Gaussian statistics, however, we do see slight divergence from Gaussian, which might be especially important for sub-threshold signals.
More systematic noise at the edge of the field of view.
Be cautious of sources under ~ 7 sigma in an image.
There is additional systematic noise when integrating over ~ a few days (patter noise).
Detector noise that mimics a burst.
BAT science Coded mask BAT products Weak sources Summary

## Slide 79: Summary
BAT is useful for many astrophysical studies
  Large field of view (~ 1/6 of the sky)
  Decent source localization (~ 3 arcmin, depends on source brightness)
  16 years of data
Coded mask technique acts differently than focusing instruments
Be cautious about sub-threshold signals and detections with low partial coding fractions.
If you have any questions, please email me: amy.y.lien@nasa.gov
BAT science Coded mask BAT products Weak sources Summary

## Slide 80: Backup

## Slide 81: Discussion
Any particular ways or objects you would like to work with BAT data?
What other BAT product you would like?
BAT science Coded mask BAT products Weak sources Summary

## Slide 82
～ 120 degree
～ 90 degree
Detector Plane Image
Reconstructed Sky Image
Deconvolute from the mask pattern
Background-subtracted
(mask-weighted) light curve
(a) Coded-mask technique
(b)
(c)
(d)
GRB

## Slide 84: BAT status update - Annual Crab calibration

## Slide 85: BAT status update - Annual Crab calibration

## Slide 86: BAT status update - Annual Crab calibration

## Slide 87: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift
Detector Plane Image (DPI)

## Slide 88: Mask-weighting analysis
Credit: NASA's Imagine the Universe and NASA/Swift

## Slide 89: Science with BAT
GRBs, counterparts for gravitational waves, fast radio bursts, tidal disruption events, AGNs, x-ray binaries…etc.
Counterpart searches
Long-term monitoring of X-ray sources.
Deep hard X-ray image from 16 years of mission time.

## Slide 90: BAT observation time

## Slide 91: BAT detector

## Slide 92: BAT sensitivity
Burst count \prop N \prop Ndet
Background count \prop N \prop Ndet
Noise \prop sqrt(N) \prop \sqrt(Ndet)
SNR \prop Ndet/sqrt(Ndet) \prop sqrt(Ndet)
Show more detail later in the survey catalog

## Slide 93: BAT data type
BAT event data  BAT GRB catalog
  Not continuous
    Event data for BAT triggers – ~ 1000 s
    Event data for sub-threshold triggers (a.k.a. failed-event data) - ~ 3 to 10 s
    Slew event data – collected during spacecraft slews (currently turned off during the pandemic)
  You can request to get event data for your observed object
  GUANO system developed at the MOC can retrieve event data retroactively if notice is sent within a few minutes from T0.
BAT rate data
  Continuous
BAT survey data  BAT survey catalog
  Continuous during spacecraft pointing mode
BAT scaled map  BAT transient monitor
  Continuous during spacecraft pointing mode
Notes: Make this into a table